## Slide 1: Leap Walking
Gesture-Based Walking
Corinna List | Daniela Neupert | Interaction Engineering | WS 17/18 | Prof. Dr. Michael Kipp

## Slide 2: Motivation
Can walking with fingers be mapped to a game character?
„Kinect“ for disabled people
Notes: We wanted to use a leap motion
We asked ourselves: How can we map the Hand to a Character -> index and middlefinger are similar to the legs
Could be a possibility for the disabled to experience a „kinect“

## Slide 3: Related Work
Noah Lockwood, Karan Singh (2012): Motion Editing with Contact Based Hand Performance
-> They used Finger-Walking to animate a character
Notes: Diffrences:
We use Leap-Motion instead of a Tabletop-Display
they only receive finger tips data
We control a game and do not create animations

## Slide 4: Concept
Map the walking-gesture to the movement of a character
Develop a jump‘n‘run-game to test the approach
Notes: To test the approach we thought it would be best to develop a game, where the user has to reach the end of a parcour
To achieve this, he has to avoid obstacles, which are high or low

## Slide 5: Setup
LeapMotion tracks best horizontally
Creating a Frame for the users orientation

## Slide 6: Interaction Techniques
Walking
Notes: 1. Calculate vector between old and current position of index and middle finger
2. Calculate angle between those two
3. angle > 90° and angle < 180° -> opposite vectors -> walking
4. Calculate speed: frequence of changes of the direction of the index finger movement

## Slide 7: Interaction Techniques
Walking Curves
Notes: We track the distance of the index finger and the pinky finger-knuckle
The user walks to the direction that the perpendicular vector is facing

## Slide 8: Interaction Techniques
Jumping
Notes: For jumping, both, the tip of the index and the tip of the middlefinger have to be away from their initial position
-> auto movement starts (automatic jump for a certain time to a certain distance)

## Slide 9: Interaction Techniques
Ducking
Notes: Ducking is detected by watching the movement of the wrist
If its next to the cardboard, the user ducks
-> auto movement starts (automatic duck for a certain time to a certain distance)

## Slide 10: Technical Realization
Leap Motion
Processing (LeapMotionForProcessing by Darius Morawiec)
Frame for the LeapMotion

## Slide 11: Demonstration
Notes: Explain briefly the GUI:
Timer that shows the start time
walked distance/total distance
hits counter
walking speed
walking direction
position of index and middle finger
2. Explain briefly the game setup:
two kinds of obstacles (user has to duck, jump or just walk around)
End reached after certain distance
3. Show the different gestures
4. Show end screen

## Slide 12: Evaluation
Difficult distinction between walking and non-walking gesture
Walking is tiring for the hand
Notes: Minor inaccurate movements of the hand may give wrong results and lead to non-walking value -> „repairing“ this issue leaded to a „slide“ after the character should already have stopped

## Slide 13: Future Work
Are there other possibilities to map the hand to the body?
Which other gestures can be used?
Could the hand positioning be different?
Thanks for your attention!
Notes: Hand positioning: e.g. rest on the arrmrest of the chair (LeapMotion positioned on the chairs armrest?)